## Slide 1: How to store Petabytes (of machine created data) ?
Maguay No-Time-for-Downtime, Sept 2021
3Q 2021

## Slide 2
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
HDD | 0.3 | 0.35 | 0.4 | 0.5 | 0.6 | 0.6 | 0.7 | 0.9 | 1 | 1.1 | 1.3 | 1.5 | 1.7 | 1.9 | 2.1 | 2.3
SSD | 0 | 0 | 0 | 0.05 | 0.03 | 0.03 | 0.05 | 0.05 | 0.1 | 0.15 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 1
NVM-NAND | 0 | 0 | 0.05 | 0.05 | 0.02 | 0.03 | 0.1 | 0.1 | 0.15 | 0.2 | 0.3 | 0.4 | 0.5 | 0.5 | 0.6 | 0.6
NVM-Other | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.05 | 0.05 | 0.05
Optical | 0.15 | 0.15 | 0.1 | 0.05 | 0.1 | 0.15 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Tape | 0.05 | 0.05 | 0.05 | 0.05 | 0.08 | 0.1 | 0.12 | 0.15 | 0.2 | 0.2 | 0.25 | 0.3 | 0.4 | 0.6 | 0.7 | 0.9
HDD
59%
SSD
NVM-NAND
Tape
Optical
22ZB
IDC forecasts that over 22ZB of storage capacity must ship across all media types from 2018 to 2025 to keep up with storage demands
Around 59% of the capacity will need to come from the HDD industry and 26% from flash technology
IDC White Paper, sponsored by Seagate, Data Age 2025: The Digitzation of the World From Edge to Core, November 2018

## Slide 3: Existing Example of “Experimental” Data

## Slide 4: The Nature of “Experimental” Data
High Amount of Data
Unstructured
Random ( no Compression, no Deduplication)
Continuously created at high, constant Rate
  (like Video Surveillance Data)
Stored for long Time
  (unlike Video Surveillance Data)
Kept online with fast and random read Access for Analytics
 IT Investment and Operations Strategy will change

## Slide 5: Storage Requirements for “Experimental” Data
“ ….the ability of Toshiba to deliver thousands of drives representing multiple petabytes – on time – is critical for the data taking and operations of the LHC”

## Slide 6
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
HDD | 0.3 | 0.35 | 0.4 | 0.5 | 0.6 | 0.6 | 0.7 | 0.9 | 1 | 1.1 | 1.3 | 1.5 | 1.7 | 1.9 | 2.1 | 2.3
SSD | 0 | 0 | 0 | 0.05 | 0.03 | 0.03 | 0.05 | 0.05 | 0.1 | 0.15 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 1
NVM-NAND | 0 | 0 | 0.05 | 0.05 | 0.02 | 0.03 | 0.1 | 0.1 | 0.15 | 0.2 | 0.3 | 0.4 | 0.5 | 0.5 | 0.6 | 0.6
NVM-Other | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.05 | 0.05 | 0.05
Optical | 0.15 | 0.15 | 0.1 | 0.05 | 0.1 | 0.15 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Tape | 0.05 | 0.05 | 0.05 | 0.05 | 0.08 | 0.1 | 0.12 | 0.15 | 0.2 | 0.2 | 0.25 | 0.3 | 0.4 | 0.6 | 0.7 | 0.9
HDD
59%
SSD
NVM-NAND
Tape
Optical
22ZB
Why (still) HDD ?
IDC White Paper, sponsored by Seagate, Data Age 2025: The Digitzation of the World From Edge to Core, November 2018

## Slide 7: HDD vs SSD: Driving Factor No. 1: Price / Capacity
Parallel prize trends for eSSD and Enterprise Capacity HDD!
SSD capacity trend:
Ultra high capacity
  16 TByte  100 Tbyte  …
Linear trend price / capacity
HDD capacity trend:
Increasing capacity
  8 TByte  10 TByte (Air)  14/16 Tbyte (He)
  18/20Tbyte (MAMR)  new technologies
At similar costs/unit
  Few 100$
Log Scale
1000
100
10
Source: TEE research & TEE estimates
10X
9X

## Slide 8: Why (still HDD) - Driving Factor No. 2: Storage Capacity
Market relies on HDDs!
How much Flash Storage can be manufactured?
2020 Total eHDD/cHDD Capacity shipped: ~1012 ExaBytes (Mio TB) in 251 Mio Units
2020 Total eSSD/cSSD Capacity shipped: ~222 ExaBytes in 387 Mio Units
Only to double SSD capacity shipped in 2020, approx. 100 billions $ additional investments for Flash fabs are required
It would cost the NAND Industry hundreds of billions of Dollars and several years of time to construct new fabrication plants to displace 100% of HDD’s installed in 2020
Within the next 5 - 10 years it will be impossible to manufacture a sufficient amount of SSDs in order to replace the installed HDD base
200mm
300mm
450mm
Investment needed for
One leading Edge Fab
>$1B
>$5B
>$10B
Source: Gartner / TEE estimates
18%

## Slide 9: 3.5” Enterprise Capacity (Nearline) Hard Disk Drives
Capacities from 1 TB to 18 TB
SAS 12 GB/s and SATA 6 GB/s Interface
7200 RPM, RV Sensors
  For continuous 24/7 Operation
  Up to 550 TB/year Workload
  Meantime to Failure up to 2.5 Mio hours
  Annualized Failure Rate down to 0.35%
  5 Year Warranty
First HDD with “Microwave assisted magnetic Recording” (MAMR)

## Slide 10: Technology for Toshiba HDD Capacity Increase
TDMR Technology
Higher storage density with two read elements to detect and cancel neighbor track interference signals.
 | 2018 | 2019 | 2021 | 
14TB
9 Disk Technology
Helium-sealed
Technology
16TB
FC-MAMR Technology
18TB
Flux Control-Microwave Assisted
Magnetic Recording
SMR Technology
Shingled Magnetic Recording
Two Dimensional Magnetic Recording

## Slide 11: Assist Recording Technology
Technology to boost disk recording capacity using microwave oscillators on magnetic heads
Technology to boost disk recording capacity using laser diode on magnetic heads
STO
(Spin torque oscillator)
Microwave
(High frequency magnetic field)
MAMR
Microwave Assisted Magnetic Recording
HAMR
Heat Assisted Magnetic Recording
Laser Diode
Wave guide
NFT
(Near field transducer)
Near-field light

## Slide 12: Future Outlook: More Platter

## Slide 13: Future Outlook: Multi Actuator
Multi-Actuator Prototype

## Slide 15: Toshiba Enterprice Capacity HDD Lineup
Options:
4k Byte Native Format
MG0xACAxxxA
MG0xSCAxxxA
SED – Self Encrypting Drives
MG0xACP / MG0xSCP
SIE – Sanitize Instant Erase
(Crypto Erase)
MG0xACAxxxEY
MG0xSCAxxxEY
SAS
12G

## Slide 16: Assist Effects of MAMR
MAMR writing assist relies on two phenomena, the well known microwave assisted
switching (MAS), and the newly highlighted flux control (FC). Oscillation rotation
angle determines relative contributions. FC dominates the assist in the MG09 writer.
Microwave Assisted Switching effect
(MAMR with MAS)
Required recording field for medium magnetization reversal is reduced by magnetic resonance between STO and media.
Original MAMR concept
Recording Flux Control effect
(MAMR with FC)
Recording field amplitude and gradient are improved by STO FC effect.
Extended concept of MAMR
Main Pole
Write Shield
STO
Medium Magnetization
Main Pole
Write Shield
STO
Medium Magnetization

## Slide 17: MAMR effects comparison
MAMR with FC (Flux Control) dominant design is for early application.
MAMR with MAS (Microwave Assisted Switching) dominant design and HAMR will be expected similar ADC potential.
 | MAMR with FC dominant design | MAMR with MAS dominant design |  | ( HAMR )
ADC gain | Up to 20% | Over 200% potential |  | Over 200% potential
Assist element reliability | Similar as Reader reliability |  |  | High temperature resistance required
Oscillation frequency control | Not necessary | Required |  | -
Media design optimization | Conventional PMR media is usable | Need MAMR optimized media (resonance frequency, uniform grain property) |  | Novel FePt granular magnetic system required
ADC: Areal Density Capability
Assisted ADC gain
2020 2025
MAMR with FC
MG09 (1st Gen) target
MAMR with MAS